DAB+ Digital Radio

with FM Transmitter

User Guide

          - DAB/DAB+ Receiver

          - Bluetooth hands-free

          - MP3 player

Feature

- The unit is with DAB/DAB+ receiver,BT play with phone hands-free and Mp3 player

- Wireless transmitter for DAB/DAB+ radio to your original car radio amplifier by FM transmission

- Receiver phone call and stream music to your car radio by Bluetooth

- Support to read music from TF card

- Line -out function to get the best sound quality connecting to car’s AUX-in

What’s in the box

dab receiver :1pcs

Car charger: 1 pcs

Car use active antenna: 1pcs

USB  line: 1 pcs

Holder: 1 pcs

Unit user guide:1 pcs

Interface introduction

| M | Press to switch mode DAB/BT/TF |
| --- | --- |
| TX | Press to search DAB channel Long-press into FM adjustment, turn konb to change transmitter freq, from 87.5-108Mhz |
| PREV | Previous channel |
| NEXT | Next channel |
| KNOB | Calling mode one -press to answer call-in Long-press to refuse to call Dobule-press to call back the last calling |

Interface introduction:

Dab antenna installation guide

It is important to install the dab antenna in the right place, it is pasted on the top left or right corner of the front windshield or the car usually, some windshield protective film has metal material, maybe weaken the signal, it’s better to remove a small piece under antenna place

- Remove the protective film of antenna

2. Pull down a pillar inner, paste the antenna in the right place

3. Ensure antenna ground contact to metal car body well

4. Install the pillar inner

Product Specification

- This digital audio broadcasting device is fully compatible with DAB ETSI 300 401 standard. Support ETSI TS102 563 DAB+ standard

- FM transmission Frequency range 87.5-108MHz

- DAB Frequency range 170-240MHz

- Receiver sensitivity -99dBm

- Color LCD display:2.4 inch 320X240 pixels

- Bluetooth ver: v4.2

- Micro USB 5V DC-in

- 3.5mm Stereo Headphone Output

- Antenna input: MCX interface car use active film antenna 3M cable.

- Temperature: 0 ℃~45℃

- Storage temperature: -20℃-70℃

- Operation relative humidity should be less than 80%(40 ℃) as storage RH less than 95%(40 ℃)

Product Maintenance

- Don’t expose the unit to the liquid, humid or moist area as the set is not waterproof.

- Don’t attempt to clean this unit with chemical solvents as this might damage the finish.

- Avoid extremes of temperature either hot or cold, recharge under normal temperature.

- Don’t touch sharp objects, which will cause scratches or damage

- Don’t attempt to insert any object into the body to avoid damage the internal parts.

- Don’t attempt to disassemble the unit for there is not any serviceable parts inside.

- If long time no use, be sure to play the unit in a dry area, avoid in temperature changes and dusty place.

- Please save after rechargeable fully when unused for a long time (one-two month), to avoid completely discharge normally which lead to open improperly or not rechargeable.